## Slide 1: Augmented Reality-assisted Human Robot Interaction
Student:
Aufar P. Laksana
CID:
01093575
Project Supervisor:
Professor Yiannis Demiris
Second Marker:
Dr. Tae-Kyun Kim
Final Year Project Presentation
Monday 24th June 2019

## Slide 2: Contents
Motivation
Project Description
High Level System Description
Breakdown of Systems
Testing & Results
Evaluation
Future Work

## Slide 3: Motivation
What is “Augmented Reality-assisted Human Robot Interaction”?
  Augmented Reality.
  Human Robot Interaction.
Personal Robotics Lab
  Research focused on the interaction between intelligent robotic devices and users operating them.
Personal Interests
  Mobile Robotics.
  Self Driving Cars/Drones.
  Not really interested in Humanoid Robots.
Notes: What is Augmented Reality-assisted Human Robot Interaction?
  A very broad title
    A broad title gives one the freedom to explore whatever they feel like, within the theme of robotics and augmented reality
    This is an undergraduate project, time limited, what do we do when one has too much freedom?
      We have to Narrow, Down, The scope
  So we begin with a definition, Augmented Reality:
    An interactive experience of real-world environments where the objects that reside in the real-world are enhanced by computer generated information, in the form of visualizations, sound, haptic feedback among other sensory
    Different from VR, which shuts out the physical world
    I recently went to Central Saint Martins, the design college at UAL, and one of the students had made an AR exhibit whereby you download an app on your phone and it transformed a 2D painting on a wall to a 3D experience you could walk through/around
    For instance, tourists in a city, using a map and you can look through your phone to see big arrows pointing where you should turn next
  Human Robot Interaction
    Self explanatory, it’s the interaction between humans and robots
    Can be things like remote interaction, such as the Mars rover, where a team of scientists and engineers are controlling something millions of kms away.
    Or a proximate interaction, such as using the humanoid robots to help people in day to day tasks
    Vast area of research, lots of cool, interesting things to explore
  Combining the two:
    Using augmented reality to enhance a humans understanding, control and interaction with robots
Personal Robotics Lab
  Research focused on the interaction between these intelligent robotic devices and the users operating them
  Some examples include:
    Teaching a humanoid robot to learn an action by copying the operator
    Using augmented reality to alert users to the state and intentions of a robot
    Assistive control by the intelligent system to help users complete tasks.
Personal Interests
  Participated in robotics competitions in high school (Botball)
    Build and program robots to complete tasks in a scenario, like recognized coloured objects and sort them to gain points
  Throughout University, became more interested in self-driving cars/drones
    Advanced Robotics course involved using the mounted camera to recognize AR markers so that the drone could locate itself in the room
  Humanoid Robots are not really my interest, they actually sort of intimidate me, a bit too lifelike

## Slide 4: Motivation (cont.)
Narrowed the scope down to:
  Augmented Reality visualizations.
  Interaction with a mobile robot.
  A bit of computer vision.
PRL Research Inspiration:
  Head-Mounted Augmented Reality for Explainable Robotic Wheelchair Assistance.
  Augmented Reality Control of Smart Wheelchair Using Eye-Gaze-Enabled Selection of Affordances.
“Power wheelchair users (PWUs) report being afraid to navigate in crowded spaces with their device” [3]
[1] M. Zolotas, J. Elsdon, and Y. Demiris. Head-mounted augmented reality for explainable robotic wheelchair assistance
[2] Rodrigo Chac´on-Quesada and Yiannis Demiris. Augmented Reality Control of Smart Wheelchair Using Eye-Gaze-Enabled Selection of Affordances
[3] Kairy, D., Rushton, P. W., (2014). Exploring powered wheelchair users and their caregivers’ perspectives on potential intelligent power wheelchair use: A qualitative study.
Notes: Factoring in all these motivations and interests, we have narrowed down the scope to:
  Augmented reality
  Interacting with a mobile robot
  Something with a bit of computer vision
In the PRL, a few of the PhD students have used the Hololens and smart wheelchair ARTA in their research
  Mark: displaying the internal states such as the planned path of the assistive control
  Rodrigo: using the Hololens to provide an interface to the user for controlling the wheelchair, such as recognizing the positions of doors and giving the user the option to go through the door using eye tracking

## Slide 5: Project Description
Augmented Reality experience using the Microsoft Hololens.
Provides assistance to powered wheelchair users (PWUs) by:
  Locating people in the surroundings.
  Displaying holograms to PWU.
Reactive control system to prevent collisions with people when operating wheelchair manually.
1
Notes: We wanted to follow the theme of robotic interaction using the powered wheelchair ARTA and the Microsoft Hololens
We also want to begin solving the problem of PWUs being afraid to navigate their devices in crowded areas.
This project involved developing an augmented reality system using the Microsoft Hololens that assists powered wheelchair users in navigating around people in crowded areas.
We utilize the Hololens as a visual input to detect and determine the positions of people in the surroundings
Using these positions, we can then use the augmented reality capabilities of the Hololens to display information to the powered wheelchair user, such as their position and the direction they are walking in relative to the PWU
We also use the knowledge of their positions to provide a simple reactive control system that prevents collisions during manual control of the wheelchair, by manipulating the speed of the device.

## Slide 6: High-level System Description
Notes: Project is split into 3 separate systems, one on running on each device:
  Hololens
    Captures the view the PWU has using front facing camera
    Maps the detected people in the surroundings
    Creates hologram visualizations
  HDD (Human Detection & Direction)
    Runs on a partner computer, receives frames from Hololens
    Processes frames by detecting people and direction relative to PWU
    Streams detections back to the Hololens
  ARTA (Assistive Robotic Transport for Adults)
    PRL smart powered wheelchair
    PWU controls the wheelchair using joystick
    Receives control signals from Hololens to avoid collisions

## Slide 7: Node View

## Slide 8: Holo: Hololens

## Slide 9: Holo: Camera Stream
Compared alternatives:
  Windows Device Portal – Latency of 2-3 seconds.
  HololensForCV, Microsoft Computer Vision library
    Designed to run on Windows using C#, standalone UWP application
    Raw sensor data streams.
    Difficulty in converting network streams between UWP and Linux.
Hololens runs the Unity Game Engine on UWP.
  Large community support for Mixed Reality and Hololens.
    Mixed Reality ToolKit (MRTK).
  Abstracts away a lot of the complicated sensor data handling.
    No need to work with raw depth values from depth camera.
  Communication handled by ROS#
    Uses ROS messaging protocols of subscribers and publishers.
    Can communicate with other ROS nodes seamlessly.

## Slide 10: Node View

## Slide 11: HDD: Human Detection & Direction
Notes: Partner PC has a GTX 1050Ti GPU
Receives captured frames from Hololens
Detects people, predicts bounding boxes
Bounding boxes are passed on
  Assign a tracking identity
  Determine if the person is facing towards/away from the PWU
Results are streamed over the network back to the Hololens

## Slide 12: HDD: Object Detector - YOLO
You Only Look Once (YOLO) Object Detector [4]
  Exhaustively searches an image and predicts bounding box and class for each grid cell.
  Runs on Darknet NN framework.
We use the Robotic Operating System (ROS) as a means of communication between devices.
  Had to port Darknet into ROS as a package to receive camera frames from Hololens.
  Writing Python wrappers around Darknet C code for ROS integration.
Trained YOLOv3-Tiny on a pedestrian detection dataset.
  CrowdHuman Dataset [5]
[4] Joseph Redmon, Santosh Kumar Divvala, Ross B. Girshick, and Ali Farhadi. You only look once: Unified, real-time object detection.
[5] Shuai Shao, Zijian Zhao, Boxun Li, Tete Xiao, Gang Yu, Xiangyu Zhang, and Jian Sun. Crowdhuman: A benchmark for detecting human in a crowd.

## Slide 13: HDD: Object Detector - YOLO
Recorded test videos using Hololens around Imperial College Campus.
  Videos were recorded while moving.
Improvements:
  Better detection of people
    At range
    Occlusions
  Head detection
    Direction prediction using head pose estimation.

## Slide 14: HDD: YACHT Tracking & Direction
Developed the Yet Another CrowdHuman Tracker (YACHT) ROS Package.
The ROS nodes consume bounding box detections from YOLO object detector node.
Deep SORT Object Tracking [6]
  Based off the Simple Online Real Time Tracking algorithm that uses an Intersection-Over-Union metric to compare bounding boxes.
  Deep network calculates a feature vector of the bounding box and finds matches by Nearest Neighbor comparison.
OpenPose Body Pose Estimation [7]
  Why Body Pose estimation?
  Used to determine if a person is walking towards/away from the camera.
Tracking ID / Direction + Bounding Box streamed over network to Hololens
[6] N. Wojke, A. Bewley, and D. Paulus. Simple online and realtime tracking with a deep association metric.
[7] Zhe Cao, Gines Hidalgo, Tomas Simon, Shih-En Wei, and Yaser Sheikh. Open- pose: Realtime multi-person 2d pose estimation using part affinity fields

## Slide 15: Node View

## Slide 16: Holo: Hololens

## Slide 17: Holo: Matching & World Placement
IOU Matching of Bounding Boxes to match Tracker ID & Direction messages.
  Possible latency between messages.
Unity GameObject created for each detected person.
  We can think of the GameObject as the representation of the person in the MR World.
  Need to correctly place GameObject relative to Hololens.
Convert a 2D image coordinate to a 3D world coordinate.
  Difficult to tell distance to object since we lose the z-axis when we capture the frame.
  Best we can do is to pass a ‘ray’ through the image point.
    Object can exist anywhere along that ray in the real world.

## Slide 18: Holo: Matching & World Placement

## Slide 19: ARTA: Reactive Control